THE SLINGSHOT ANTENNA
146-148mhz

        Please note in drawing that elements are bent 90 degrees. Make your bends as needed depending on material used for elements. If you use copper tubing, a 90 degree elbow on each should work fine. If you are comfortable with bending, great, if not, get the hardware store to do it for you!

The completed antenna is bi-directional with a rough figure 8 pattern and is composed of 2, 3/4 wavelength sections of electrical conduit bent and cut to the lengths in the drawing and supported as shown on any type of insulating material attached to the mast with whatever arrangement of bolts, nuts, clamps, etc.
You should note that the bottom (horizontal element portion) is 1/4 wavelength long and the top (vertical element section) is 1/2 wavelength long.
The element mounting plate (in yellow in the drawing) can be Plexiglas, painted wood or whatever you happen to have that is NON CONDUCTIVE.  You can use copper or aluminum for the active 3/4 wave elements, but aluminum would be preferred due to less weight.
Although electrical conduit comes in various sizes, the size was not stated in the original article but I would suggest 1/2 inch or larger in diameter. (The larger, the greater the bandwidth.)
The total length of each element is 60 inches + - and they are attached about 4 inches apart on the mounting plate with enough bolts and nuts as needed.
The coax attachment points are in red on the picture, and I would suggest that you use spade lugs on the ends of the coax to attach it to the bottom end of each element (the ends nearest the bend) with bolts, nuts and lock washers all the way thru the element and plate. There must be a good electrical connection between the coax center conductor and shield braid and each element. Keep the connections lengths from the end of the coax as short as possible. They become part of the radiating element lengths.
It does not matter which conductor from the coax is attached to which element.
SEAL ALL CONNECTIONS AND THE END OF THE COAX!
When attaching the elements to the mounting plate, drill enough holes all the way thru the elements and plate for good mechanical stability and attach with bolts and nuts. The elements and coax connections must not touch the support mast at any point if the mast is made of metal of any kind! You could use a PVC pipe or length of lumber of the required length instead of metal to get the antenna up as high as possible and a half wave or more is preferred!
"This design, untrimmed, up a half wave, presented an SWR of 1.5:1 across the top 2 MHZ of the band (146-148mhz)"
.......KA8OGD